## Slide 1: TIOVX – TI’s OpenVX Implementation
18 June 2018
Kedar Chitnis, Jesse Villarreal
Automotive Processors, ADAS
NOTE: Some slides are
“TI Confidential – NDA Restrictions”

## Slide 2: Agenda
Introduction to OpenVX
OpenVX example use-case on TI SoC
TI OpenVX Implementation Overview
OpenVX on different TI SoCs
TI OpenVX Implementation Details
OpenVX and other frameworks (OpenCL/CV/…)
Getting Started with TI OpenVX
Summary
Notes: OpenVX has this idea of computation graphs, where image operations called nodes process data.
The nodes may be dedicated HW blocks, or if they run for example on a GPU, they may be written in OpenCL.
The application first sets up a graph, telling system in advance which type of processing it will want to perform.
The system then has a possibility to work on the processing graph, to spend some effort to optimize the total graph, before executing it.
The host, the CPU, needs only pass in some data, and then can idle, while the OpenVX subsystem, in more power-efficient HW, autonomously executes the graph.

## Slide 3: Introduction to OpenVX

## Slide 4: OpenVX – Low-Power Vision Acceleration
Higher-level abstraction API
  Targeted at real-time mobile and embedded platforms
Performance portability across diverse architectures
  Multi-core CPUs, GPUs, DSPs, ISPs, Dedicated hardware, …
Extends portable vision acceleration to very low-power domains
  Doesn’t require high-power CPU/GPU Complex
  Lower precision requirements than OpenCL
Accelerator
Vision Engine
Middleware
Application
Accelerator
Accelerator
Power Efficiency
Computation Flexibility
Dedicated Hardware
GPU Compute
Multi-core
CPU
X1
X10
X100
Vision Processing Efficiency
Vision DSPs
Notes: OpenVX is a special API for low-power vision acceleration.
It is a fairly high-level API, especially compared to programming language approach like with OpenCL, and it is aimed to provide real-time computer vision support on mobile and embedded devices.
The API abstracts the underlying hardware, the implementation can use multi-core CPUs, or GPUs, or DSPs, or ISPs, or some new dedicated computer vision HW.
But the programmer doesn’t have to care exactly how the API is implemented, the device manufacturers take care of those details instead.
Now even very low-power wearable devices can address vision workloads without involving the high-power CPU/GPU complex.
As OpenVX has lower precision requirements than OpenCL, it is mostly fixed-point API, whereas OpenCL is mostly a floating-point API, in OpenVX computations can be done with simpler, lower-power HW.

## Slide 5: OpenVX Graphs
OpenVX developers express a graph of image operations (‘Nodes’)
  Nodes can be on any hardware or processor coded in any language
  For example, on GPU, nodes may implemented in OpenCL
Minimizes host interaction during frame-rate graph execution
  Host processor can setup graph which can then execute almost autonomously
Array of
Keypoints
YUV
Frame
Gray
Frame
Camera Input
Rendering
Output
Pyrt
Color Conversion
Channel Extract
Optical Flow
Harris Track
Image
Pyramid
RGB
Frame
Array of
Features
Ftrt-1
OpenVX Graph
OpenVX Nodes
Notes: OpenVX has this idea of computation graphs, where image operations called nodes process data.
The nodes may be dedicated HW blocks, or if they run for example on a GPU, they may be written in OpenCL.
The application first sets up a graph, telling system in advance which type of processing it will want to perform.
The system then has a possibility to work on the processing graph, to spend some effort to optimize the total graph, before executing it.
The host, the CPU, needs only pass in some data, and then can idle, while the OpenVX subsystem, in more power-efficient HW, autonomously executes the graph.

## Slide 6: An OpenVX “Hello, World !!!” Program
context
vx_context context = vxCreateContext();
vx_graph graph = vxCreateGraph( context );
vx_image input = vxCreateImage( context, 640, 480, VX_DF_IMAGE_U8 );
vx_image output = vxCreateImage( context, 640, 480, VX_DF_IMAGE_U8 );
vx_image intermediate = vxCreateVirtualImage( graph, 640, 480, VX_DF_IMAGE_U8 );
vx_node F1 = vxF1Node( graph, input, intermediate );
vx_node F2 = vxF2Node( graph, intermediate, output );
vxVerifyGraph( graph );
vxProcessGraph( graph );
output
input
F1
F2
graph
inter-
mediate
Notes: First, we create a context for the OpenVX operations and data, and then we start a graph in that context.
We then create the input image, the output image, and an intermediate, virtual image, that we will never look at.
We then add two nodes, the first one connecting input to intermediate, the second the intermediate to output.
We then verify the graph, and now the system can perform optimizations, such as tiling, etc.
Finally, we process the graph.

## Slide 7: OpenVX Pipelining Extension
Provide a way of Pipelining, streaming, and batch processing
Multiple initiations of a graph with different inputs and outputs
Increase hardware utilization and throughput
Example SoC, with three independent
Heterogeneous compute units
Executes
OpenVX Graph
Without Pipelining extension
With Pipelining extension

## Slide 8: More Details on OpenVX Standard
Khronos OpenVX website
  https://www.khronos.org/openvx/
OpenVX v1.1 specification and additional resources
  https://www.khronos.org/registry/OpenVX/
  https://www.khronos.org/openvx/resources
Khronos OpenVX v1.1 Video Tutorials
  https://youtu.be/JZZCNcfIqqs?list=PLYO7XTAX41FP01wTyWfwiNW3xq9IDRAnO

## Slide 9: OpenVX Example Use-case on TI SoC

## Slide 10: Heterogeneous Multi-Core System Example
Multiple computation cores each used depending on its suitability for that compute functions
Goal is to balance performance with power consumption on embedded devices
TI TDAxx SoC
ISP
HWA
DSP
DSP
ARM
Pixels
Pixels
Feature Vector
Classified output
Decision/Control
Post Processing HWA
HW Accelerator

## Slide 11: Mono-camera Analytics Processing Graph (Example)

## Slide 12: TI OpenVX Implementation Overview

## Slide 13: TIOVX - OpenVX Implementation on TI SoC
GOAL: Help customers easily maximize performance on TI platforms while minimizing development cost.
Result: Full entitlement on TI SoCs and remove barrier to entry for OpenVX developers
Performance
Graph-based model
Maximizes system utilization and minimizes run-time latencies.
True Heterogeneous Compute
Unified access to all ARM, DSP, Vision/HWA
Optimized Libraries
Development Cost
Open Standard
Conformant to OpenVX v1.1 with support for graph pipelining extension
Hardware Abstraction
Same application works across TDA2x/3x family of SoCs on range of SW environments from Linux to TI-RTOS
Ease of use
Full development, including DSP intrinsic emulation, can be done on PC using TI OpenVX, then simple recompile on platform.
PyTIOVX tool generates OpenVX Application/Kernel code
Fully optimized OpenVX 1.1 kernels on DSP
DMA Integration
Simple interface to add block-based DMA to kernels (BAM)

## Slide 14: TI OpenVX Supported Platforms
OpenVX v1.1
Target CPUs
OS
TDA2x
TDA2Eco
TDA3x

## Slide 15: TI OpenVX SW Stack on TDA2x/3x
TIOVX Kernel Wrapper
TIOVX Framework
Context
Node
Graph
OpenVX API
Khronos Conformance Test
Kernel
Image
Scalar
Array
Pyramid
…
Khronos
TI
Examples / Use-cases with Processor SDK - Vision
TIOVX Platform
Memory
Obj Desc
Event
Mutex
IPC
VXLIB
EVELIB
User kernels
Customer
Examples / Use-cases with Processor SDK - Vision
Task
Queue
Platform
Target
Target Kernel
TIOVX API
TI Extension Conformance Test
Target kernels

## Slide 16: VXLIB Overview
Scope of VXLIB
  Lowest level algorithm library (like VLIB, IMGLIB, DSPLIB)
  Only dependency is compiler
    No OS dependency, no memory allocation, no DMA dependency
  Implements OpenVX 1.1 kernels on DSP
  Will also implement additional DSP vision kernels
    OpenCV acceleration, Support DSP algorithms, etc.
Supported Targets
  C66 DSP (elf)
  Host emulation support:
    X86/X64 MSVC (windows)
    X86/x86_64 GCC (linux)
Conformance
  MISRAC Compliant (Klocwork static analysis)

## Slide 17: VXLIB - Kernel List
VXLIB_absDiff_i16s_i16s_o16s
VXLIB_absDiff_i8u_i8u_o8u
VXLIB_accumulateImage_i8u_o16s
VXLIB_accumulateSquareImage_i8u_o16s
VXLIB_accumulateWeightedImage_i8u_o8u
VXLIB_add_i16s_i16s_o16s
VXLIB_add_i8u_i16s_o16s
VXLIB_add_i8u_i8u_o16s
VXLIB_add_i8u_i8u_o8u
VXLIB_addSquare_i8u_i16s_o16s
VXLIB_addWeight_i8u_i8u_o8u
VXLIB_and_i8u_i8u_o8u
VXLIB_box_3x3_i8u_o8u
VXLIB_cannyNMS_i16s_i16s_i16u_o8u
VXLIB_channelCombine_1to1_i8u
VXLIB_channelCombine_2to1_i8u
VXLIB_channelCombine_3to1_i8u
VXLIB_channelCombine_4to1_i8u
VXLIB_channelCombine_yuyv_i8u
VXLIB_channelExtract_o8u
VXLIB_colorConvert_IYUVtoNV12_i8u_o8u
VXLIB_colorConvert_IYUVtoRGB_i8u_o8u
VXLIB_colorConvert_IYUVtoYUV4_i8u_o8u
VXLIB_colorConvert_NVXXtoIYUV_i8u_o8u
VXLIB_colorConvert_NVXXtoRGB_i8u_o8u
VXLIB_colorConvert_NVXXtoRGBX_i8u_o8u
VXLIB_colorConvert_NVXXtoYUV4_i8u_o8u
VXLIB_colorConvert_RGBtoIYUV_i8u_o8u
VXLIB_colorConvert_RGBtoNV12_i8u_o8u
VXLIB_colorConvert_RGBtoRGBX_i8u_o8u
VXLIB_colorConvert_RGBtoYUV4_i8u_o8u
VXLIB_colorConvert_RGBXtoRGB_i8u_o8u
VXLIB_colorConvert_YUVXtoIYUV_i8u_o8u
VXLIB_colorConvert_YUVXtoNV12_i8u_o8u
VXLIB_colorConvert_YUVXtoRGB_i8u_o8u
VXLIB_colorConvert_YUVXtoRGBX_i8u_o8u
VXLIB_convertDepth_16to8
VXLIB_convertDepth_8to16
VXLIB_convolve_3x3_i8u_c16s_o16s
VXLIB_convolve_3x3_i8u_c16s_o8u
VXLIB_convolve_5x5_i8u_c16s_o16s
VXLIB_convolve_5x5_i8u_c16s_o8u
VXLIB_convolve_7x7_i8u_c16s_o16s
VXLIB (114)
VXLIB_convolve_7x7_i8u_c16s_o8u
VXLIB_convolve_i8u_c16s_o16s
VXLIB_convolve_i8u_c16s_o8u
VXLIB_dilate_3x3_i8u_o8u
VXLIB_doubleThreshold_i16u_i8u
VXLIB_edgeTracing_i8u
VXLIB_equalizeHist_i8u_o8u
VXLIB_erode_3x3_i8u_o8u
VXLIB_fastCorners_i8u
VXLIB_fastCornersDetect_i8u
VXLIB_fastCornersNMS_i8u
VXLIB_fastCornersScore_i8u
VXLIB_gaussian_3x3_i8u_o8u
VXLIB_gaussian_5x5_i8u_o8u
VXLIB_halfScaleGaussian_5x5_i8u_o8u
VXLIB_harrisScore_i16s_i16s_o32f
VXLIB_harrisScore_i32s_i32s_o32f
VXLIB_histogram_i8u_o32u
VXLIB_histogramCdfLut_i32u_o8u
VXLIB_histogramSimple_i8u_o32u
VXLIB_integralImage_i8u_o32u
VXLIB_magnitude_i16s_i16s_o16s
VXLIB_meanStdDev_i8u_o32f
VXLIB_median_3x3_i8u_o8u
VXLIB_minMaxLoc_i16s
VXLIB_minMaxLoc_i8u
VXLIB_multiply_i16s_i16s_o16s
VXLIB_multiply_i8u_i16s_o16s
VXLIB_multiply_i8u_i8u_o16s
VXLIB_multiply_i8u_i8u_o8u
VXLIB_normL1_i16s_i16s_o16u
VXLIB_normL2_i16s_i16s_o16u
VXLIB_not_i8u_o8u
VXLIB_or_i8u_i8u_o8u
VXLIB_phase_i16s_i16s_o8u
VXLIB_remapBilinear_bc_i8u_i32f_o8u
VXLIB_remapNearest_bc_i8u_i32f_o8u
VXLIB_scaleImageBilinear_bc_i8u_o8u
VXLIB_scaleImageBilinear_br_i8u_o8u
VXLIB_scaleImageBilinear_i8u_o8u
VXLIB_scaleImageNearest_i8u_o8u
VXLIB_sobel_3x3_i8u_o16s_o16s
VXLIB_sobel_5x5_i8u_o16s_o16s
VXLIB_sobel_7x7_i8u_o16s_o16s
VXLIB_sobel_7x7_i8u_o32s_o32s
VXLIB_sobelX_3x3_i8u_o16s
VXLIB_sobelY_3x3_i8u_o16s
VXLIB_subtract_i16s_i16s_o16s
VXLIB_subtract_i8u_i16s_o16s
VXLIB_subtract_i8u_i8u_o16s
VXLIB_subtract_i8u_i8u_o8u
VXLIB_tableLookup_i16s_o16s
VXLIB_tableLookup_i8u_o8u
VXLIB_thresholdBinary_i8u_o8u
VXLIB_thresholdRange_i8u_o8u
VXLIB_warpAffineBilinear_bc_i8u_c32f_o8u
VXLIB_warpAffineBilinear_i8u_c32f_o8u
VXLIB_warpAffineNearest_bc_i8u_c32f_o8u
VXLIB_warpAffineNearest_i8u_c32f_o8u
VXLIB_warpPerspectiveBilinear_bc_i8u_c32f_o8u
VXLIB_warpPerspectiveBilinear_i8u_c32f_o8u
VXLIB_warpPerspectiveNearest_bc_i8u_c32f_o8u
VXLIB_warpPerspectiveNearest_i8u_c32f_o8u
VXLIB_xor_i8u_i8u_o8u
HarrisCorners
OpticalFlowLK
LaplacianPyramid
LaplacianReconstruct
Median
Erode
Dilate

## Slide 18: TI OpenVX on different TI SoCs

## Slide 19: TI OpenVX – Abstract “Thread” View
HOST
(OpenVX API)
Target 1
Target 2
Target 4
Target 3
HOST-TARGET CMDs.
TARGET-TARGET CMDs
(Subset of HOST-TARGET CMDs)
HOST
Target
User Thread on HOST CPU, calls OpenVX APIs
TI OpenVX “Target” Thread.
A target executes a OpenVX node
A target can run on same CPU as HOST.
Multiple targets can run on same CPU.
Targets execute in parallel to each other.

## Slide 20: TI OpenVX on TDA3x
HOST (IPU1-0)
(OpenVX API)
Target DSP1
Target IPU1-0
Target
DSP2
Target EVE1
HOST
Target
User Thread on HOST CPU, calls OpenVX APIs
TI OpenVX “Target” Thread. Can run on same CPU as HOST. Multiple Target on a CPU possible. Target execute in parallel to each other
HOST-TARGET CMDs.
TARGET-TARGET CMDs
(Subset of HOST-TARGET CMDs)

## Slide 21: TI OpenVX on TDA2x
Target
A15
Target DSP1
Target IPU1-0
Target
DSP2
Target EVE1
Target EVE2
Target
A15
Here OpenVX APIs is called by HOST on A15 optionally running HLOS like Linux
HOST (A15)
(OpenVX API)

## Slide 22: TI OpenVX Implementation on TDA4x
TI Confidential – NDA Restrictions

## Slide 23: TI OpenVX on TDA4x TI SoC
TI Confidential – NDA Restrictions
Target DSP C7x
Target
…
Target HWA
CSI2RX
Target ARM
Target HWA VPAC
Target HWA DMPAC
DSP (C6x, C7x), ARM (R5F, Axx), HWAs (DMPAC, VPAC, MMA) will be exported as OpenVX nodes
VXLIB on C6x DSP will run OpenVX compliant kernels
Streaming camera capture and display will also be exported as OpenVX
Graph pipeline and streaming extension will allow OpenVX nodes to pipelined across frames at system level
User kernels can be run on DSP, ARM and other SW programmable nodes on the SoC
HOST (ARM A72)
(OpenVX API)

## Slide 24: TI OpenVX SW Stack – TDA4x Platform
TIOVX Kernel Wrapper
TIOVX Framework
Context
Node
Graph
OpenVX API
Khronos Conformance Test
Kernel
Image
Scalar
Array
Pyramid
…
Khronos
TI
Examples / Use-cases with Processor SDK Automotive
TIOVX Platform
Memory
Obj Desc
Event
Mutex
IPC
VXLIB
NF
User kernels
Customer
Examples / Use-cases with Processor SDK Automotive
Task
Queue
Platform
Target
Target Kernel
TIOVX API
TI Extension Conformance Test
Target kernels
MSC
LDC
VISS
SDE
DOF
TIDL
Camera
Display
TI Confidential – NDA Restrictions

## Slide 25: Pipelined Graph Execution in TDA4x
OpenVX Application
Target
A15
OpenVX Camera
Target DSP1
Target DSS
Target
DSP2
Target CSI2RX
Target HWA
Target
ARM
OpenVX compute nodes
OpenVX Display
OpenVX extension for graph pipelining supports pipelined graph execution with capture and display
Complete application can be written using OpenVX APIs
Pipelined execution of OpenVX nodes with camera and display improves system utilization
TDA4x SoC
TI Confidential – NDA Restrictions

## Slide 26: TDA4x OpenVX Application Development Flow
TIOVX Kernel Wrapper
TIOVX Framework
OpenVX API
TIOVX Platform Abstraction Layer (x86)
VXLIB
TIDL
Vision HWA
User kernels
OpenVX Parking Spot Detect Application
TI
Customer
HWA Bit exact C Models (x86)
VISS
VPAC LDC
DMPAC SDE
VPAC MSC
VPAC NF
DMPAC DOF
C6x / C7x / MMA x86 model
OpenVX App …
x86-64 Linux PC
TIOVX Kernel Wrapper
TIOVX Framework
OpenVX API
TIOVX Platform Abstraction Layer (J7 / TDA4x)
VXLIB
TIDL
Vision HWA
User kernels
OpenVX Parking Spot Detect Application
HWA Drivers (R5F)
VISS
VPAC LDC
DMPAC SDE
VPAC MSC
VPAC NF
DMPAC DOF
C6x / C7x / MMA
CPU
OpenVX App …
TDA4x / J7 SoC
Develop and test kernels, application on x86 PC
Run on J7 / SoC without modifications
TI Confidential – NDA Restrictions

## Slide 27: TI OpenVX Case Study: Park Space Detect on TDA4x
TI Confidential – NDA Restrictions

## Slide 28: Demo Setup
Sensors
Fisheye Camera
Novatel INS
TI Confidential – NDA Restrictions

## Slide 29: Functional Blocks Diagram (J7 / TDA4x)
Heavy weight processing is offloaded to HWA such as optical flow, pyramids, undistort…etc.
>80% processing on HWA & <20% on DSP/ARM enables >5X power reduction!!
Dense Optical Flow HWA creates highly accurate (industry leading) & dense (full image points) flow map.
Vision HWA enables lower latency pipleline vs. processing in programmable compute.
TI Confidential – NDA Restrictions

## Slide 30: Implementation with OpenVX
Each processing element is implemented as a OpenVX Node
OpenVX node enables platform portability and Ease of Development
TI OpenVX graph approach enables connected nodes with fewer trips to external memory or host processor – Lower Latency
TI OpenVX nodes for Jacinto 7 IP is available using simulation models.
TI OpenVX graph toolkit is available Now!
TI Confidential – NDA Restrictions

## Slide 31: Parking Spot Detect Demo Screenshots
LIDAR
High accurate depth map (OG map) using TI HWA (Dense Optical Flow, VPAC, …).
Correlates well with LIDAR map (see right side) – Industry leading KPIs
Offloads >80% processing on Hardware accelerators - Lowest power embedded solution, Scalable
Camera
TI Confidential – NDA Restrictions

## Slide 32: TI OpenVX Implementation Details

## Slide 33: Mono-camera Analytics Processing Graph (Example)

## Slide 34: Distributed Graph Execution
Distributed graph execution minimizes overheads at “HOST” ARM CPU and reduces system latency
DSP1
DSP2
EVE1
ISS
M4
IMG PP
SOF
FPC
IMG PYR
PD
TSR
VD
OC
TLR
LD
SFM
FCW
DRAW
vxScheduleGraph
vxWaitGraph
NOT TO SCALE
(1)
(1)
(2)
(3)
(3)
(4)
(5)
(6)
(7)
CPU Idle

## Slide 35: Block Access Manager (BAM) Framework
Non-BAM based programming model
DSP
Compute Unit
L2 Cache
Big External memory
Data I/O
Data I/O
BAM framework based programming model
Big External memory
On-chip
L2 RAM
DMA
Data I/O
Data I/O
Data I/O
DSP
Divides an input into smaller 2-D blocks and pipelines kernels using BAM
BAM manages DMA, including abstracting the overlap reads required for filtering kernels.
Reduces the input/output accesses made in the external memory
"Virtual Image” in OpenVX is used to eliminate intermediate buffers.
Most OpenVX v1.1 kernels optimized on DSP using BAM
Compute Unit

## Slide 36: PyTIOVX - Automated OpenVX “C” Code Generation
PyTIOVX
Generated C code can run on SoC without modifications
Visualize graph connections
Trap and fix common mistakes before executing on target SoC

## Slide 37: TI OpenVX and other frameworks

## Slide 38: Pipelined Graph Execution with Processor SDK – Vision (TDA2x/3x)
OpenVX Link
Target
A15
Camera Link
Target DSP1
Target ARM M4
Target
DSP2
Target EVE1
Target EVE2
Target
ARM A15
OpenVX Application
Display Link
OpenVX used for compute
Processor SDK – Vision used for Camera, Display, system level control
Pipelined execution of OpenVX with camera and display improves system utilization
TDA2x SoC

## Slide 39: TI OpenVX with Customer Frameworks
OpenVX API (HOST)
ARM
Customer SW Stack
DSP
Customer SW Stack
OpenVX Framework
OpenVX Kernel Wrapper
OpenVX Targets can be enabled only on required CPUs, HWAs
On the same CPU, an OpenVX as well as other customer threads/algorithms can co-exists
Customers can plugin their own algorithms as OpenVX nodes
  Existing algorithms can be used as-is with a OpenVX kernel wrapper
When not using TI Vision SDK framework, minor porting in “platform” layer of OpenVX may be required to make OpenVX work with customer framework
Customer Kernels
OpenVX Framework
OpenVX Kernel Wrapper
Customer Kernels
OpenVX Application
Reuse customer SW
New customer SW
TI SW

## Slide 40: TI OpenVX with OpenCL on TDA2x (Example)
Target A15
Target DSP1
Target IPU1-0
Target A15
Target EVE1
Target EVE2
Target
OpenCL (A15)
HOST (A15)
(OpenVX API)
OpenCL Device
DSP1
OpenCL Device
DSP2
Here OpenVX kernel on Target OpenCL (A15) offloads work to DSPs running OpenCL using OpenCL framework
Target A15 is used for generic compute on A15

## Slide 41: TI OpenVX with OpenCV on TDA2x (Example)
Target
A15
Target DSP1
Target IPU1-0
Target
DSP2
Target EVE1
Target EVE2
Target
A15
Here OpenCV APIs can be called by OpenVX nodes running on HOST
HOST (A15)
(OpenVX API)
OpenCV API
(A15)

## Slide 42: Getting Started with TI OpenVX

## Slide 43: TIOVX within Processor SDK - Vision
TIOVX is present in Processor SDK – Vision at the location shown below
TIOVX package

## Slide 44: TIOVX Getting Started
TIOVX sample application can be run on Linux x86 PC as well as TI TDA2x/3x SoC/EVM
Follow steps in user guide to run sample applications on Linux x86 PC or SoC/EVM

## Slide 45: TIOVX Sample Applications
main() for Khronos conformance test suite, including TI extension test suite on Linux x86 PC
Helps confirm installation is fine and TI implementation meets OpenVX conformance
main() for TI OpenVX Step-by-step Tutorials on Linux x86 PC
Recommended starting point to learn TI OpenVX

## Slide 46: TIOVX Tutorials
Step by step examples to understand OpenVX, followed TI extensions to OpenVX including developing kernels on TI C6xx DSP
Load and Save VX images
Image manipulation using VXU APIs
Image manipulation using graph and VX node APIs
Graph with multiple targets, DSP1 and DSP2
Graph generated with PyTIOVX tool
Graph with user kernels on ARM
Graph with target kernels on DSP

## Slide 47: TIOVX on TI SoC/EVM
TI OpenVX sample application entry point to run on TI SoC/EVM can be found within Processor SDK – Vision
RTOS OpenVX applications
Embedded Linux OpenVX applications

## Slide 48: TIOVX on TI SoC/EVM with Capture and Display
A TI OpenVX sample application shows interaction of OpenVX with links framework for capture and display.
\vision_sdk\apps\src\rtos\usecases\vip_single_cam_openvx
OpenVX use-case with capture and display “links”
OpenVX “link” used in the use-case
\vision_sdk\apps\src\rtos\alg_plugins\openvx

## Slide 49: Summary and Additional Resources

## Slide 50: Summary
TI OpenVX supports true multi-core heterogeneous compute on TDA2x/3x and next gen TI SoCs
TI OpenVX implementation differentiates via
  Distributed graph execution
  DMA acceleration using BAM
  Pipelined graph execution and streaming IO nodes (camera/display)
  Ease of use via code generation (PyTIOVX) tool, PC emulation mode
  Ability to run on “Big ARM” CPUs with HLOS as well as “MCU ARM” CPUs using RTOS
TI OpenVX is included as part of Processor SDK – Vision on TDA2x/3x SoCs

## Slide 51: Additional TIOVX Resources
Release notes – READ this first
  \tiovx_xx_xx_xx_xx\tiovx_release_notes.html
User guide, tutorial guide, PyTIOVX guide
  \tiovx_xx_xx_xx_xx\docs\user_guide\index.html
  \tiovx_xx_xx_xx_xx\docs\tutorial_guide\index.html
  \tiovx_xx_xx_xx_xx\docs\pytiovx_guide\index.html
Processor SDK – Vision resources
  \vision_sdk\docs\Index.htm
Web resources
  http://www.ti.com/processors/automotive-processors/tdax-adas-socs/overview.html
  https://training.ti.com/openvx-implementation-ti-tda-adas-socs
  http://www.ti.com/tool/processor-sdk-vision
  https://e2e.ti.com/support/arm/automotive_processors/f/1021

## Slide 52: Thank You !!!

## Slide 53: Revision History
Date | Version | Author | Remarks
13 Jun 2016 | 0.50 | Kedar C | First draft
23 Aug 2016 | 0.60 | Kedar C | Added revision history
26 Aug 2016 | 0.70 | Kedar C | Added conceptual view on different SoCs and interaction with other frameworks
21 Sept 2016 | 0.82 | Kedar C | Edited to make it friendly for sharing with customers. Separated Net Gen TI SoC information in a separate slide. Added slides on co-existence with customer SW stacks.
23 Sept 2016 | 0.83 | Kedar C | Removed references to “ASIL” and made it “Safety ready”
29 Nov 2016 | 0.90 | Kedar C | Updated based on current implementation progress
10 Jan 2017 | 1.00 | Kedar C | Updated based on current implementation progress
15 Jan 2017 | 1.01 | Kedar C | TIOVX Stack updated
13 Mar 2017 | 1.02 | Kedar C | Minor updates
3 Apr 2017 | 1.03 | Kedar C | Updates based on current status and plans
7 Jun 2017 | 1.04 | Kedar C | Minor update in block diagram
28 Jun 2017 | 1.05 | Kedar C | Updated plans based on aligned features
7 Nov 2017 | 1.06 | Kedar C | Updated based on latest updates
23 May 2018 | 1.08 | Kedar C | Updated based on latest updates
18 Jun 2018 | 1.09 | Kedar C | Added details on parking space detect OpenVX demo

## Slide 54: TI OpenVX Implementation Plan
Milestone | Features | Schedule
Phase 1 | OpenVX v1.1 on TDA2x/3X SoCs with Processor SDK – Vision 3.x | AVAILABLE NOW
Phase 2 | Enable TDA4x “PC Emulation” of HWAs, C7x | AVAILABLE NOW
Phase 3 | Additional enhancements (ex, graph pipelining, TIDL) | Q2 2018
Phase 4 | Additional enhancements (ex, camera/display nodes) | Q1 2019
Phase 5 | OpenVX on J7/TDA4x with Processor SDK Automotive | Q3 2019
* Schedule and features are preliminary and subject to change
TI Confidential – NDA Restrictions