## Slide 1: TIOVX – TI’s OpenVX Implementation
28 Sept 2017

## Slide 2: Agenda
Introduction to OpenVX
OpenVX on TI SoCs – TIOVX
Getting Started with TIOVX
Notes: OpenVX has this idea of computation graphs, where image operations called nodes process data.
The nodes may be dedicated HW blocks, or if they run for example on a GPU, they may be written in OpenCL.
The application first sets up a graph, telling system in advance which type of processing it will want to perform.
The system then has a possibility to work on the processing graph, to spend some effort to optimize the total graph, before executing it.
The host, the CPU, needs only pass in some data, and then can idle, while the OpenVX subsystem, in more power-efficient HW, autonomously executes the graph.

## Slide 3: Agenda
Introduction to OpenVX
OpenVX on TI SoCs – TIOVX
Getting Started with TIOVX
Notes: OpenVX has this idea of computation graphs, where image operations called nodes process data.
The nodes may be dedicated HW blocks, or if they run for example on a GPU, they may be written in OpenCL.
The application first sets up a graph, telling system in advance which type of processing it will want to perform.
The system then has a possibility to work on the processing graph, to spend some effort to optimize the total graph, before executing it.
The host, the CPU, needs only pass in some data, and then can idle, while the OpenVX subsystem, in more power-efficient HW, autonomously executes the graph.

## Slide 4: OpenVX – Low-Power Vision Acceleration
Higher-level abstraction API
  Targeted at real-time mobile and embedded platforms
Performance portability across diverse architectures
  Multi-core CPUs, GPUs, DSPs, ISPs, Dedicated hardware, …
Extends portable vision acceleration to very low-power domains
  Doesn’t require high-power CPU/GPU Complex
  Lower precision requirements than OpenCL
Accelerator
Vision Engine
Middleware
Application
Accelerator
Accelerator
Power Efficiency
Computation Flexibility
Dedicated Hardware
GPU Compute
Multi-core
CPU
X1
X10
X100
Vision Processing Efficiency
Vision DSPs
Notes: OpenVX is a special API for low-power vision acceleration.
It is a fairly high-level API, especially compared to programming language approach like with OpenCL, and it is aimed to provide real-time computer vision support on mobile and embedded devices.
The API abstracts the underlying hardware, the implementation can use multi-core CPUs, or GPUs, or DSPs, or ISPs, or some new dedicated computer vision HW.
But the programmer doesn’t have to care exactly how the API is implemented, the device manufacturers take care of those details instead.
Now even very low-power wearable devices can address vision workloads without involving the high-power CPU/GPU complex.
As OpenVX has lower precision requirements than OpenCL, it is mostly fixed-point API, whereas OpenCL is mostly a floating-point API, in OpenVX computations can be done with simpler, lower-power HW.

## Slide 5: OpenVX Graphs
OpenVX developers express a graph of image operations (‘Nodes’)
  Nodes can be on any hardware or processor coded in any language
  For example, on GPU, nodes may implemented in OpenCL
Minimizes host interaction during frame-rate graph execution
  Host processor can setup graph which can then execute almost autonomously
Array of
Keypoints
YUV
Frame
Gray
Frame
Camera Input
Rendering
Output
Pyrt
Color Conversion
Channel Extract
Optical Flow
Harris Track
Image
Pyramid
RGB
Frame
Array of
Features
Ftrt-1
OpenVX Graph
OpenVX Nodes
Notes: OpenVX has this idea of computation graphs, where image operations called nodes process data.
The nodes may be dedicated HW blocks, or if they run for example on a GPU, they may be written in OpenCL.
The application first sets up a graph, telling system in advance which type of processing it will want to perform.
The system then has a possibility to work on the processing graph, to spend some effort to optimize the total graph, before executing it.
The host, the CPU, needs only pass in some data, and then can idle, while the OpenVX subsystem, in more power-efficient HW, autonomously executes the graph.

## Slide 6: An OpenVX “Hello, World !!!” Program
context
vx_context context = vxCreateContext();
vx_graph graph = vxCreateGraph( context );
vx_image input = vxCreateImage( context, 640, 480, VX_DF_IMAGE_U8 );
vx_image output = vxCreateImage( context, 640, 480, VX_DF_IMAGE_U8 );
vx_image intermediate = vxCreateVirtualImage( graph, 640, 480, VX_DF_IMAGE_U8 );
vx_node F1 = vxF1Node( graph, input, intermediate );
vx_node F2 = vxF2Node( graph, intermediate, output );
vxVerifyGraph( graph );
vxProcessGraph( graph );
output
input
F1
F2
graph
inter-
mediate
Notes: First, we create a context for the OpenVX operations and data, and then we start a graph in that context.
We then create the input image, the output image, and an intermediate, virtual image, that we will never look at.
We then add two nodes, the first one connecting input to intermediate, the second the intermediate to output.
We then verify the graph, and now the system can perform optimizations, such as tiling, etc.
Finally, we process the graph.

## Slide 7: More Details on OpenVX Standard
Khronos OpenVX website
  https://www.khronos.org/openvx/
OpenVX v1.1 specification and additional resources
  https://www.khronos.org/registry/OpenVX/
  https://www.khronos.org/openvx/resources
Khronos OpenVX v1.1 Video Tutorials
  https://youtu.be/JZZCNcfIqqs?list=PLYO7XTAX41FP01wTyWfwiNW3xq9IDRAnO

## Slide 8: Agenda
Introduction to OpenVX
OpenVX on TI SoCs – TIOVX
Getting Started with TIOVX
Notes: OpenVX has this idea of computation graphs, where image operations called nodes process data.
The nodes may be dedicated HW blocks, or if they run for example on a GPU, they may be written in OpenCL.
The application first sets up a graph, telling system in advance which type of processing it will want to perform.
The system then has a possibility to work on the processing graph, to spend some effort to optimize the total graph, before executing it.
The host, the CPU, needs only pass in some data, and then can idle, while the OpenVX subsystem, in more power-efficient HW, autonomously executes the graph.

## Slide 9: TIOVX - OpenVX Implementation on TI SoC
GOAL: Help customers easily maximize performance on TI platforms while minimizing development cost.
Result: Full entitlement on TI SoCs and remove barrier to entry for OpenVX developers
Performance
Graph-based model
All work defined at initialization time to maximize system utilization and minimize run- time latencies.
True Heterogeneous Compute
Easy/unified access to all ARM, DSP, Vision (EVE) Cores
Optimized Libraries
Development Cost
Open Standard
Conformant to OpenVX v1.1
Hardware Abstraction
Same application works across TDA2x/3x family of SoCs on range of SW environments from Linux to TI-RTOS
Ease of use
Full development, including DMA, DSP/EVE intrinsic emulation, can be done on PC using TI OpenVX, then simple recompile on platform.
PyTIOVX tool generates OpenVX Application code using compact graph description
Fully optimized OpenVX 1.1 kernels on C6x DSP
DMA Integration
Simple interface to add block-based DMA to kernels (BAM)
Virtual Buffers
Intermediate buffers can be optimized out, or reside only in L2.

## Slide 10: OpenVX 1.1 Supported Platforms
OpenVX
Target CPUs
OS
TDA2x
TDA2Eco
TDA3x

## Slide 11: TI OpenVX SW Stack
TIOVX Kernel Wrapper
TIOVX Framework
Context
Node
Graph
OpenVX API
Khronos Conformance Test
Kernel
Image
Scalar
Array
Pyramid
…
Khronos
TI
Examples / Use-cases with Processor SDK - Vision
TIOVX Platform
Memory
Obj Desc
Event
Mutex
IPC
VXLIB
EVELIB
User kernels
Customer
Examples / Use-cases with Processor SDK - Vision
Task
Queue
Platform
Target
Target Kernel
TIOVX API
TI Extension Conformance Test
Target kernels

## Slide 12: TI OpenVX on TDA3x
HOST (IPU1-0)
(OpenVX API)
Target DSP1
Target IPU1-0
Target
DSP2
Target EVE1
HOST-TARGET CMDs.
TARGET-TARGET CMDs
HOST
Target
User Thread on HOST CPU, calls OpenVX APIs
TI OpenVX “Target” executes vision kernels. Target can run on same CPU as HOST. Multiple Targets on a CPU possible. Target execute in parallel to each other

## Slide 13: Mono-camera Analytics Processing Graph (Example)

## Slide 14: Distributed Graph Execution
Distributed graph execution minimizes overheads at “HOST” ARM CPU and reduces system latency

## Slide 15: Block Access Manager (BAM) Framework
Non-BAM based programming model
DSP
Compute Unit
L2 Cache
Big External memory
Data I/O
Data I/O
BAM framework based programming model
Big External memory
On-chip
L2 RAM
DMA
Data I/O
Data I/O
Data I/O
DSP
Divides an input into smaller 2-D blocks and pipelines kernels using BAM
BAM manages DMA, including abstracting the overlap reads required for filtering kernels.
Reduces the input/output accesses made in the external memory
"Virtual Image” in OpenVX is used to eliminate intermediate buffers.
Most OpenVX v1.1 kernels optimized on DSP using BAM
Compute Unit

## Slide 16: PyTIOVX - Automated OpenVX “C” Code Generation
PyTIOVX
Generated C code can run on SoC without modifications
Visualize graph connections
Trap and fix common mistakes before executing on target SoC

## Slide 17: Pipelined Graph Execution with Processor SDK - Vision
OpenVX Link
Target
A15
Camera Link
Target DSP1
Target ARM M4
Target
DSP2
Target EVE1
Target EVE2
Target
ARM A15
OpenVX Application
Display Link
OpenVX used for compute
Processor SDK – Vision used for Camera, Display, system level control
Pipelined execution of OpenVX with camera and display improves system utilization
TDA2x SoC

## Slide 18: Summary
TI OpenVX supports true multi-core heterogeneous compute on TDA2x/3x SoCs
TI OpenVX implementation differentiates via
  Distributed graph execution
  DMA acceleration using BAM
  Pipelined graph execution and streaming IO nodes (camera/display)
  Ease of use via code generation (PyTIOVX) tool, PC emulation mode
  Ability to run on “Big ARM” CPUs with HLOS as well as “MCU ARM” CPUs using RTOS

## Slide 19: Agenda
Introduction to OpenVX
OpenVX on TI SoCs – TIOVX
Getting Started with TIOVX
Notes: OpenVX has this idea of computation graphs, where image operations called nodes process data.
The nodes may be dedicated HW blocks, or if they run for example on a GPU, they may be written in OpenCL.
The application first sets up a graph, telling system in advance which type of processing it will want to perform.
The system then has a possibility to work on the processing graph, to spend some effort to optimize the total graph, before executing it.
The host, the CPU, needs only pass in some data, and then can idle, while the OpenVX subsystem, in more power-efficient HW, autonomously executes the graph.

## Slide 20: TIOVX within Processor SDK - Vision
TIOVX is present in Processor SDK – Vision at the location shown below
TIOVX package

## Slide 21: TIOVX Getting Started
TIOVX sample application can be run on Linux x86 PC as well as TI TDA2x/3x SoC/EVM
Follow steps in user guide to run sample applications on Linux x86 PC or SoC/EVM

## Slide 22: TIOVX Sample Applications
main() for Khronos conformance test suite, including TI extension test suite on Linux x86 PC
Helps confirm installation is fine and TI implementation meets OpenVX conformance
main() for TI OpenVX Step-by-step Tutorials on Linux x86 PC
Recommended starting point to learn TI OpenVX

## Slide 23: TIOVX Tutorials
Step by step examples to understand OpenVX, followed TI extensions to OpenVX including developing kernels on TI C6xx DSP
Load and Save VX images
Image manipulation using VXU APIs
Image manipulation using graph and VX node APIs
Graph with multiple targets, DSP1 and DSP2
Graph generated with PyTIOVX tool
Graph with user kernels on ARM
Graph with target kernels on DSP

## Slide 24: TIOVX on TI SoC/EVM
TI OpenVX sample application entry point to run on TI SoC/EVM can be found within Processor SDK – Vision
RTOS OpenVX applications
Embedded Linux OpenVX applications

## Slide 25: TIOVX on TI SoC/EVM with Capture and Display
A TI OpenVX sample application shows interaction of OpenVX with links framework for capture and display.
\vision_sdk\apps\src\rtos\usecases\vip_single_cam_openvx
OpenVX use-case with capture and display “links”
OpenVX “link” used in the use-case
\vision_sdk\apps\src\rtos\alg_plugins\openvx

## Slide 26: Additional TIOVX Resources
Release notes – READ this first
  \tiovx_xx_xx_xx_xx\tiovx_release_notes.html
User guide, tutorial guide, PyTIOVX guide
  \tiovx_xx_xx_xx_xx\docs\user_guide\index.html
  \tiovx_xx_xx_xx_xx\docs\tutorial_guide\index.html
  \tiovx_xx_xx_xx_xx\docs\pytiovx_guide\index.html
Processor SDK – Vision resources
  \vision_sdk\docs\Index.htm
Web resources
  http://www.ti.com/processors/automotive-processors/tdax-adas-socs/overview.html
  http://www.ti.com/tool/processor-sdk-vision
  https://e2e.ti.com/support/arm/automotive_processors/f/1021

## Slide 27: Thank You !!!